## Slide 1
TCP Basics
Mayank Pandey
MNNIT Allahabad, Prayagraj, India

## Slide 2: Recap:
Connectionless and Connection oriented MUX/DEMUX (Concept of Ports)
UDP (User Datagram Protocol)
Pseudo-header and Checksum
Developing a Reliable Data Transport (RDT) Protocol from scratch: The FSM way.
Pipelined Protocols:
  GBN (Go Back N)
  SR (Selective Repeat)

## Slide 3: Transmission Control Protocol (TCP)
Service Model:
  Connection Orientation Connection Abstraction
    Illusion of connection over connection less Internet
  Byte stream Abstraction
    no record markers or message boundaries
    Packetization and Re-packetization
  Reliable and Ordered Delivery
    Sequence numbers, ACKs, Retransmission
  Point to Point with Full duplex
  Protocol Implemented Entirely at Ends

## Slide 4: TCP Encapsulation

## Slide 5: TCP Header

## Slide 6: TCP Header
Source Port, Destination Port
  The source and destination port number, along with the source and destination IP addresses in the IP header, uniquely identify each connection
The combination of an IP address and a port number is called
  an endpoint or socket in the TCP literature
    The term "socket" appeared in [RFC0793]
    ultimately adopted as the name of the Berkeley-derived programming interface for network communications (called "Berkeley sockets").
    It is a pair of sockets or endpoints (the 4-tuple consisting of the client IP address, client port number, server IP address, and server port number) that uniquely identifies each TCP connection.
    Important when multiple clients are connecting to a server.

## Slide 7: TCP Header
The Sequence Number field
  identifies the byte in the stream of data
    from the sending TCP to the receiving TCP
    TCP numbers each byte with a sequence number.
    Sequence number of first byte in any segment represents the sequence number of that segment
This sequence number is a 32-bit unsigned number that wraps back around to 0 after reaching (232) − 1.
  More on it later ( This space can be extended using TCP options)

## Slide 8: TCP Header
The Acknowledgment Number field
  contains the next sequence number
    that the sender of the acknowledgment expects to receive.
    This is therefore the sequence number of the last successfully received byte of data plus 1 (Different from GBN)
    This field is valid only if the ACK bit field is on
  Sending an ACK costs nothing more than sending any other TCP segment
    the 32-bit ACK Number field is always part of the header,
    as is the ACK bit field.

## Slide 9: TCP Header: Flags
Currently eight bit fields are defined for the TCP header, older implementations understand only the last six of them:
  CWR. Congestion Window Reduced ( sender reduced its sending rate)
  ECE. ECN Echo (the sender received an earlier congestion notification)
  URG. Urgent (the Urgent Pointer field is valid; rarely used)
  ACK. Acknowledgment (the Acknowledgment Number field is valid, always on after a connection is established)
  PSH. Push (the receiver should pass this data to the application as soon as possible; not reliably implemented or used)
  RST. Reset the connection (connection abort, usually because of an error)
  SYN. Synchronize sequence numbers to initiate a connection
  FIN. The sender of the segment is finished sending data to its peer.

## Slide 10: TCP Header
The Header Length field
  length of the header in 32-bit words.
    required because the length of the Options field is variable.
    With a 4-bit field, TCP is limited to a 60-byte header.
      ?????
  Without options, the size is 20 bytes.

## Slide 11: TCP Header
Window Size field
  Used for TCP’s flow control
    number of bytes, starting with the one specified by the ACK number that the receiver is willing to accept.
    16-bit field, limiting the window to 65,535 bytes
      and thereby limiting TCP’s throughput performance.
    Window Scale option (More Later)

## Slide 12: TCP Header (Other Fields)
The TCP Checksum field
  TCP header and data and some fields
    in the IP header using a pseudo-header computation.
The Urgent Pointer field
  valid only if the URG flag bit field is set
  This "pointer" is a positive offset
    must be added to the Sequence Number field of the segment
      to yield the sequence number of the last byte of urgent data.

## Slide 13: TCP Options
Will be covered in a separate lecture.
Maximum Segment Size (MSS) Option
Selective Acknowledgment (SACK) Options
Window Scale (WSCALE or WSOPT) Option
Timestamps Option and Protection against Wrapped Sequence Numbers (PAWS)
User Timeout (UTO) Option
Authentication Option (TCP-AO)

## Slide 14: Evolution of TCP
1975
1980
1985
1990
1982
TCP & IP
RFC 793 & 791
1974
TCP described by
Vint Cerf and Bob Kahn
In IEEE Trans Comm
1983
BSD Unix 4.2
supports TCP/IP
1984
Nagel’s algorithm
to reduce overhead
of small packets;
predicts congestion collapse
1987
Karn’s algorithm
to better estimate round-trip time
1986
Congestion collapse
observed
1988
Van Jacobson’s algorithms
congestion avoidance and congestion control
(most implemented in 4.3BSD Tahoe)
1990
4.3BSD Reno
fast retransmit
delayed ACK’s
1975
Three-way handshake
Raymond Tomlinson
In SIGCOMM 75

## Slide 15: TCP Through the 1990s
1993
1994
1996
1994
ECN
(Floyd)
Explicit
Congestion
Notification
1993
TCP Vegas
(Brakmo et al)
real congestion avoidance
1994
T/TCP
(Braden)
Transaction
TCP
1996
SACK TCP
(Floyd et al)
Selective Acknowledgement
1996
Hoe
Improving TCP startup
1996
FACK TCP
(Mathis et al)
extension to SACK

## Slide 16: TCP Usage Model
Connection setup
  3-way handshake
Data transport
  Sender writes data and TCP
    Breaks data into segments
    Sends each segment over IP
    Retransmits, reorders and removes duplicates
  Receiver reads data
Teardown
  4 step exchange

## Slide 17: TCP Connection Setup

## Slide 18: TCP Connection Setup
  The active opener (client)
    sends a SYN segment (SYN bit field turned on)
      specifying the port number of the peer to which it wants to connect and the client’s initial sequence number or ISN(c)
      It typically sends one or more options at this point. This is segment 1.
  The passive opener (server) responds with its
    own SYN segment containing its initial sequence number (ISN(s)).
      also acknowledges the client’s SYN by ACKing ISN(c) plus 1. This is segment 2.
  The client must acknowledge this SYN
    from the server by ACKing ISN(s) plus 1. This is segment 3.

## Slide 19: TCP Connection Setup
Initial Sequence Number:
  The Sequence Number field in SYN segment
    contains the first sequence number to be used on that direction of the connection
      for subsequent sequence numbers and in returning ACK numbers.
      This number is not 0 or 1 but instead is another number
      often randomly chosen, called the initial sequence number (ISN).
      The reason for the ISN not being 0 or 1: ????

## Slide 20: TCP Connection Setup
MSS option (most commonly used)
  Each end of a connection specifies this option with the SYN segment.
  The MSS option specifies
    maximum-size segment, end host is willing to receive in the reverse direction.
  Typically set to
    (MTU of directly connected network – size of TCP and IP headers)
      TCP_MAXSEG socket option

## Slide 21: TCP Connection Termination

## Slide 22: TCP Connection Termination
The active closer sends a FIN segment
  specifying the current sequence number the receiver expects to see (K)
  FIN also includes an ACK for the last data sent in the other direction (L)
The passive closer responds by
  ACKing value K + 1: successful receipt of the active closer’s FIN.
  The passive closer then effectively becomes another active closer and sends its own FIN. The sequence number is equal to L.
  To complete the close, the final segment contains an ACK for the last FIN.
  if a FIN is lost, it is retransmitted until an ACK for it is received.
Berkley Sockets: close() and shutdown() system calls, TCP Half close:
"I am done sending data, so send a FIN to the other end, but I still want to receive data from the other end, until it sends me a FIN."

## Slide 23: Flow/Congestion/Error Control
Flow Control
  Algorithms to prevent that the sender overruns the receiver with information
Error Control
  Algorithms to recover from or conceal the effects from packet losses
Congestion Control
  Algorithms to prevent that the sender overloads the network
The goals of each control mechanisms are different
  In TCP, the implementation of these algorithms is combined

## Slide 24: Acknowledgements in TCP
TCP receivers use acknowledgments (ACKs)
  to confirm the receipt of data to the sender
Acknowledgment can be added (“piggybacked”) to
  a data segment that carries data in the opposite direction
ACK information is included in TCP header
Acknowledgements are used for
  flow control, error control, and congestion control

## Slide 25: Cumulative Acknowledgements
SeqNo=0 10 bytes
TCP has cumulative acknowledgements:
  An acknowledgment confirms the receipt of all unacknowledged data with a smaller sequence number
A
B
SeqNo=10 10 bytes
ACK 10
ACK 20
ACK 40
ACK 70
ACK 100
SeqNo=20 10 bytes
SeqNo=30 10 bytes
SeqNo=40 10 bytes
SeqNo=50 10 bytes
SeqNo=60 10 bytes
SeqNo=70 10 bytes
SeqNo=80 10 bytes
SeqNo=90 10 bytes

## Slide 26: Cumulative Acknowledgements
With cumulative ACKs
  the receiver can only acknowledge a segment if all previous segments have been received
  receiver cannot selectively acknowledge blocks of segments:
    e.g., ACK for S0-S3 and S5-S7 (but not for S4)
The use of cumulative ACKs imposes constraints on the retransmission schemes:
  In case of an error, the sender may need to
    retransmit all data that has not been acknowledged

## Slide 27: TCP Flow Control

## Slide 28: TCP Flow Control
TCP uses a version of the sliding window flow control, where
  Sending acknowledgements is separated from setting the window size at sender
  Acknowledgements do not automatically increase the window size
During connection establishment, both ends of a TCP connection set the initial size of the sliding window

## Slide 29: Window Management in TCP
The receiver is returning two parameters to the sender
The interpretation is:
    I am ready to receive new data with
    SeqNo= AckNo, AckNo+1, …., AckNo+Win-1

## Slide 30: Sliding Window Flow Control
Sliding Window Protocol is performed at the byte level:
Here: Sender can transmit sequence numbers 6,7,8.

## Slide 31: Sliding Window: “Window Closes”
Transmission of a single byte (with SeqNo = 6) and acknowledgement is received (AckNo = 5, Win=4):

## Slide 32: Sliding Window: “Window Opens”
Acknowledgement is received that enlarges the window to the right (AckNo = 5, Win=6):
A receiver opens a window when TCP buffer empties (meaning that data is delivered to the application).

## Slide 33: Sliding Window: “Window Shrinks”
Acknowledgement is received that reduces the window from the right (AckNo = 5, Win=3):
Shrinking a window should not be used

## Slide 34: Sliding Window: Example
Zero window Advertisement
Persistence Timer……Then Zero Window Probe (More on this Later)

## Slide 35: Sliding Window: Bit more details
SND.WND
  gives the number of unacknowledged packets
SND.UNA
  represents first unacknowledged packet
SND.NXT represents the sequence number of next packet
  which can be sent without waiting for any acknowledgement.

## Slide 36: Sliding Window: Important Issue
usable_window = SND.UNA + SND.WND − SND.NXT
= 20+17-29 = 8
Suppose in the snapshot of previous slide:
  There is a ZWA (Zero Window Advertisement)
  Which also acknowledges 25
  It makes usable window negative (26+0-29 = -3)
According to RFC 793 and RFC 1122, shrinking of window is discouraged.
It is stated that TCP receiver should not shrink the window.
However, TCP sender should be robust against any such window shrinking (which causes negative usable window).
This unclear statement of RFC lead to variations in TCP implementations

## Slide 37: Error Control in TCP
TCP maintains a Retransmission Timer for each connection:
  The timer is started during a transmission. A timeout causes a retransmission
TCP couples error control and congestion control (i.e., it assumes that errors are caused by congestion)
  Retransmission is part of congestion control algorithm
Here: How to set the timeout value of the retransmission timer?

## Slide 38: TCP Retransmission Timer
Retransmission Timer:
  The setting of the retransmission timer is crucial
  Timeout value too small  unnecessary retransmissions
  Timeout value too large  long waiting time before a retransmission can be issued
  A problem is that the delays in the network are not fixed
    Therefore, the retransmission timers must be adaptive
    (More on it Later)

## Slide 39: TCP ACK generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediate send ACK, provided that
segment starts at lower end of gap

## Slide 40: TCP Congestion Control

## Slide 41: TCP Congestion Control
TCP has a mechanism for congestion control.
  The mechanism is implemented at the sender
The window size at the sender is set as follows:
Send Window = MIN (flow control window, congestion window)
where
  flow control window
    is advertised by the receiver
  congestion window
    is adjusted based on feedback from the network

## Slide 42: TCP Congestion Control Algorithms
The standard TCP implementations today follow RFC 2581.
  This reference document specifies four standard congestion control algorithms that are now in common use.
  The four algorithms are:
  Slow Start
  Congestion Avoidance
  Fast Retransmit
  Fast Recovery

## Slide 43: TCP Congestion Control
TCP congestion control is governed by
  Congestion Window (cwnd)
  Slow-start threshhold Value (ssthresh)
  Initial value is 216-1
Congestion control works in two modes:
  slow start (cwnd < ssthresh)
  congestion avoidance (cwnd ≥ ssthresh)

## Slide 44: Slow Start
Initial value: Set cwnd = 1
  Each time an ACK is received by the sender
    the congestion window is increased by 1 segment:
    cwnd = cwnd + 1
Does Slow Start increment slowly?
  Not really.
    In fact, the increase of cwnd is exponential

## Slide 45: Slow Start Example
The congestion window size grows very rapidly
TCP slows down the increase of cwnd when cwnd > ssthresh

## Slide 46: Congestion Avoidance
Congestion avoidance phase is started if
  cwnd has reached the slow-start threshold value
If cwnd ≥ ssthresh then each time an ACK is received
  increment cwnd as follows:
    cwnd = cwnd + 1/ cwnd
So cwnd is increased by one only if all cwnd segments have been acknowledged.

## Slide 47: Example
Assume that ssthresh = 8
Roundtrip times
Cwnd (in segments)
ssthresh

## Slide 48: Responses to Congestion
TCP assumes there is congestion if it detects a packet loss
A TCP sender can detect lost packets via:
    Timeout of a retransmission timer
    Receipt of a duplicate ACK

## Slide 49: Responses to Congestion
TCP interprets a Timeout as a binary congestion signal
  When a timeout occurs, the sender performs:
    cwnd is reset to one:
      cwnd = 1
    ssthresh is set to half the current size of the congestion window:
      ssthressh = cwnd / 2
    and slow-start is entered

## Slide 50: Summary : Congestion Control
Initially:
cwnd = 1;
ssthresh = advertised window size;
New Ack received:
if (cwnd < ssthresh)
/* Slow Start*/
cwnd = cwnd + 1;
else
/* Congestion Avoidance */
cwnd = cwnd + 1/cwnd;
Timeout:
/* Multiplicative decrease */
ssthresh = cwnd/2;
cwnd = 1;

## Slide 51: Fast Retransmit
If three or more duplicate ACKs are received in a row
  TCP sender believes that a segment has been lost.
TCP performs a retransmission of what seems to be the missing segment
  without waiting for a timeout to happen.
Enter slow start:
  ssthresh = cwnd/2
  cwnd = 1

## Slide 52: Fast Recovery
Fast recovery avoids slow start after a fast retransmit
  Intuition: Duplicate ACKs indicate that data is getting through
After three duplicate ACKs set:
  Retransmit packet that is presumed lost
  ssthresh = cwnd/2
  cwnd = cwnd/2 +3
  Increment cwnd by one for each additional duplicate ACK
When ACK arrives that acknowledges “new data”
  cwnd=ssthresh and enter congestion avoidance

## Slide 53: Comparison (TCP Variants)
Tahoe:
  Slow start, congestion avoidance and fast retransmit
Reno:
  Tahoe + fast recovery
New-Reno:
  Reno with modified fast recovery
SACK:
  Reno + selective ACKs

## Slide 54: Tahoe:
On new ack:
if (cwnd < sstresh)
-- cwnd += 1
else
-- cwnd += 1/cwnd
On timeout/3rd dup ack:
-- retransmit all unacked
-- ssthresh = cwnd/2
-- cwnd = 1

## Slide 55: Reno: Improving TCP Tahoe
Packets still getting through in dup ack
  no need to reset the clock!
On new ack:
if (cwnd < sstresh)
-- cwnd += 1
else
-- cwnd += 1/cwnd

## Slide 56: Reno:
timeout:
  retransmit 1st unacked
  ssthresh = cwnd/2
  cwnd = 1
3rd dup ack:
  retransmit 1st unacked
  ssthresh = cwnd/2
  cwnd = cwnd/2 + 3

## Slide 57: Reno:
subsequent dup ack:
  cwnd++
new ack:
  cwnd = ssthresh

## Slide 58: TCP With SACK
Based on RFC 2018
  (TCP Selective Acknowledgement Options) –standards track
Good for when multiple packets are lost
  from one window of data
Gives sender view of
  which segments queued at receiver and which in flight
Uses two TCP options
  “SACK permitted”
    may be sent in a SYN segment
  SACK option itself
    may be sent over an established connection
Notes: SACK option itself, which may be sent over an established connection one permission has been given
By SACK-permitted

## Slide 59: SACK Options : Format
Sack-permitted option
  Two bytes option
    Sack option itself (Kind = 5, Length=variable)
Kind = 2
Length = 4
Length
Kind = 5
Left edge of 1st block
Right edge of 1st block
Right edge of nth block
Left edge of nth block

## Slide 60: SACK Options : Examples
Assume the left edge is 5000 and transmitter sends a burst of 8 segments, each containing 500 data bytes
Example (1) The first four segments are received but the last 4 are dropped
The data receiver will return a normal TCP ACK segment acknowledging sequence number 7000, with no SACK option

## Slide 61: SACK Options : Examples
Example (2) The first segment is lost but the remaining 7 segments are received.
Receiver will return a TCP ACK segment that acknowledges sequence number 5000 and contains SACK option specifying one block of queued data
LE = Left Edge
RE = Right Edge

## Slide 62: SACK Options : Examples
Example (3)The 2nd, 4th, 6th and 8th (last) segments are dropped.
First block
Second block
Third block
Left
Edge
Right
Edge
Left
Edge
Left
Edge
Right
Edge
Right
Edge
SACK not used
6000
6500
7000
7500
6000
6500
8000
8500
7000
7500
6000
6500
(a)
(b)
(c)
(d)

## Slide 63: SACK Options : Examples
Suppose at this point (continue from pervious example) the 4th packet is received out of order.
Receiver replies with the following SACK:
First block
Second block
Third block
Left
edge
Right
edge
Left
edge
Right
edge
Left
edge
Right
edge
ACK
5500
6000
8000
7500
8500

## Slide 64: SACK Options : Examples
Suppose that the 2nd segment is received.
  Receiver replies with the following SACK:
7500
8000
8500
First block

## Slide 65: SACK Blocks
1st block - report most recently received segments
subsequent blocks – repeat most recent previous blocks